## Slide 1: MODHMS Working Files

## Slide 2
The raw data for the top layer elevation needs to be mirrored in X

## Slide 3
Define a new variable Xnew to mirror the elevation data

## Slide 4
Assign Xnew as the X-axis variable.

## Slide 5
Write the Y (V2), cell elevation (V3), Xnew to a new file

## Slide 6
Move the Xnew column to the left side and rename the varibles X, Y and Cell Elevation
Save this as ‘new elevation_MUT_001.dat’

## Slide 7
Load the template mesh into Tecplot
Load the cell elevation points

## Slide 8
Interpolate using Inverse Distance because Kriging did not work

## Slide 9
Convert and save the file so it can be read by ‘elevation from list file’ instruction
Write the cell elevations to a file

## Slide 10
Run mut _build
Load build.lay
Contour GWF cell top